## Slide 1
Livestock and Poultry Expansion: Critical Issues for Discussion with Farmers & Communities
Preparations for today:
Open Chat Box – access to handouts and ask questions.
Mute microphone during presentation, unmute during Q&A
View archived presentations, obtain handouts: http://water.unl.edu/livestock-poultry-expansion-critical-issues-discussion-farmers-and-communities and click on Agenda
Join us for our next webinar on Monday, July 25, 2016 (Noon CDT)
Siting Facilities for Biosecurity
  Sheila Purdum: Into to AI and other siting considerations
  Renee Hancock: Planning for Mortality

## Slide 2: Site Visit: Applying Principles to the Farm
Hosted by Bill Bevans, farmer & poultry producer (near Lincoln)
Hear from Bill about issues important to him. Use maps and aerial photos to evaluate alternative sites.
Meet from 1 to 3 PM
Date to be determined by Doodlehttp://doodle.com/poll/h5429zz799trgnr8

## Slide 3: Site Considerations for Managing Manure Nutrients
Richard K. Koelsch, Bio. Systems Engr. and Animal Science, University of Nebraska

## Slide 4: My Purpose
What is our goal?
Two Questions to assist potential animal producer during planning process:
  How much land will a grower need access?
  Will buffer/setback expectations allow for manure application?

## Slide 5
What Is Our Goal?
Recycle Nutrients and Carbon
Balancing field Imports with crop requirements:
Balance N annually.
Balance P annually, if practical, or over 3 to 5 year period
Limit Edge of Field Loss
Building soil carbon and pH
Manure
Crop
Fertilizer
Other N Sources
Edge of Field Loss
X

## Slide 6: The Nebraska Advantage: The Opportunity to Recycle
Integrated crop & livestock allows recycling of nutrients
Fertilizer & Feed

## Slide 7: Separating animals & feed has created ag’s most challenging water quality issues
< Crop needs
Approaching
Crop Needs
> Crop Needs
?
Counties where Manure P is:

## Slide 8: How much land will animal facility need access?
Animals Excreted N/yr Excreted P2O5/yr
1,000 cow dairy 347,000 128,000
1,000 beef cattle 56,000 16,000
100,000 layers 125,000 87,000
100,000 broilers 71,000 52,000
1,000 finishing pigs 26,000 9,600

## Slide 9: How much land will animal facility need access?
Animals Land for N* Land for P*
1,000 cow dairy 1,300 ac 2,100 ac
1,000 beef cattle 100 ac 270 ac (open lot)
130 ac 270 ac (barn)
100,000 layers 530 ac 1,400 ac
100,000 broilers 60 ac 810 ac
1,000 finishing pigs 110 ac 160 ac
* Applied to 200 bushel/ac corn

## Slide 10: Four broiler barns – 176,000 birds capacity
Excreted
  125,000 lb N /yr
  91,000 lb P2O5/yr
Delivered to field
  35,000 lb N/yr
  87,000 lb P2O5/yr
Land Required:
  110 acres for N
  1,400 acres for P

## Slide 11: Go to “Software” web page http://water.unl.edu/manure/software#nutrient Look under “Nutrient Inventory”

## Slide 12: Buffers or Setbacks
?
?
Title 130: Manure is “not to be applied within 100’ of down-gradient surface waters, tile intakes, sinkholes, well heads, or other conduits to surface water”. 35 foot grassed buffer is option to 100 foot no application zone.

## Slide 13: Setbacks & Grass Buffers Needed?
???

## Slide 14: Take Home Message – N & P Exports
Our ability to recycle manure nutrients & carbon is a Nebraska’s advantage.
Help producer answer:
How many acres are needed to recycle N & P?
Will setback/buffer requirements eliminate some fields from consideration?

## Slide 15
Questions & Comments
Richard K. Koelsch, University of Nebraska, rkoelsch1@unl.edu, 402/472-3935

## Slide 16: What Principles Should Guide Nutrient Plans of the future?
Minimize environmental impact of nutrients
Satisfy public (& regulatory) expectations
Document farm’s sustainability?
  Measurable metrics?
  Efficient use of inputs?
  Continuous improvement?
  Communicate to consumer?